This generic Safety Data Sheet has been provided for information purposes only, since according to present legislation the producer is under no obligation to provide any SDS for this material. The company issuing the SDS has the full responsibility to ensure the SDS is according to latest EU legislation and information about the substances listed.

1. Identification of the substance/preparation and of the company/undertaking

1.1 Product identifier

Aluminium oxide, Alumina

Additional trade names: calcined alumina

Article code: reference to materials standards

REACH Registration No.: 01-2119529248-35-xxxx

1.2 Use of the substance/ the preparation

Industrial use, further processing into a number of articles/products

Primary aluminium production

1.3 Manufacturer / Supplier:

1.3.1 Company:	 	xyz

Street: 			bbb 2

Postal Code/Location:	xxx / zzz

phone:

fax:

1.3.2 Further information obtainable from:

phone + 00 xxxxxxxxxxxxxxx

E-Mail (expert): xxx@yyy.com

1.3.3 Information in case of emergency

Call national emergency number (include national emergency number in the national language version)

2. Hazards Identification

2.1 Classification

. Not classified.

2.2 Information concerning particular hazards for human and environment:

Does not pose any health hazard under normal conditions of use and as delivered.

High dust concentration may cause mechanical irritation of the eyes, skin and respiratory tract

3. Composition/information on ingredients

3.1 Chemical characterisation:

Aluminium oxide content of > 95 weight by weight %

3.2 Ingredients:

| CAS # | EC # | Component | Concentration % | Classification | R- phrase |
| --- | --- | --- | --- | --- | --- |
| 1344-28-1 | 215-691-6 | Aluminium oxide (non-fibrous) | > 95 | --- --- | --- --- |

3.3 Additional information:

Usually supplied to customers in bulk or big bags. Main impurities iron oxide, sodium oxide, silicon and calcium oxide

4. First-aid measures

4.1 General information:

First aide personnel: pay attention to self- protection!

- After inhalation: In case of dust inhalation remove to ventilated area and keep calm. In case of ongoing discomfort consult a physician

- After skin contact: In case of large exposures wash with soap and water.

- After eye contact: If particles comes into contact with eyes treatment for mechanical irritation or injury may be required; flush thoroughly with water, in case of ongoing discomfort consult a physician

- After swallowing: Wash mouth with water.

4.2 Notes to physician:

None

5. Fire-fighting measures

Not flammable.

5.1 Suitable extinguishing agents:

Use extinguishing agents appropriate for surrounding materials.

5.2 For safety reasons unsuitable extinguishing agents:

None

5.3 Special hazards caused by the substance, its products of combustion or resulting gases:

None.

5.4 Protective equipment:

Fire fighters should wear approved personal protective equipment for the surrounding fired material,

5.5 Additional hints:

6. Accidental release measures

6.1 Person- related safety precautions:

See protection measures listed in section 8.

6.2 Environmental protection measures:

Avoid dispersal of spilled material and runoff. Avoid creating dusty conditions and prevent wind dispersal. Collect material for recycling if possible.

6.3 Measures for cleaning:

Use vacuum cleaner if possible. .

6.4 Additional hints:

See section 13

7. Handling and storage

7.1 Handling:

Ensure good ventilation / local exhaust at the workplace in the case of operations generating dust.  Avoid creating dusty conditions. Avoid inhalation and skin and eye contact

Wear appropriate personal protective equipment. Do not add wet alumina to electrolysis cells

7.2 Storage

Requirements to be met by storerooms and receptacles:

Store in dry area.

Additional hints:

None

8. Exposure controls/personal protection

8.1 Exposure limits

Occupational exposure limits (air): generally same as for nuisance dust

Germany

10*/3** mg/m3 (*inhalable dust; ** respirable dust)

Great Britain

10*/4** mg/m3 (*inhalable dust; ** respirable dust)

United States

OSHA	15 mg/m3 (total dust); 5 mg/m3 TWA (respirable fraction)

Some additional EU countries: 10 mg/m3   (include national OEL if this exists)

8.2 Exposure controls:

Ensure good ventilation / local exhaust at the workplace in the case of operations generating dust. Avoid work practises which generate dust. Avoid inhalation and particles entering the eyes

8.3 Personal protective equipment:

Respiratory equipment: not required under recommended conditions of use. In case dust is generated, use personal protective equipment, dust filter P2 or if fine particles P3.

Use protective goggles and gloves when handling the substance and appropriate work clothes

8.4 Environmental exposure control:

Avoid creating dusty conditions and prevent wind dispersal and dust emissions.

9. Physical and chemical properties

9.1 General information:

Physical state: 	solid powder

Colour: 		white

Odour: 		odourless

pH- value: 			not relevant

Melting point/Melting range: 	approx. 2030°C

Boiling Point/Boiling range: 	not relevant

Flash point: 			not relevant

Flammability:			not relevant

Explosive properties:		not relevant

Density at 20°C: 			3,99 g/cm3

Solubility in water (20 °C): 		insoluble

Other physical–chemical properties: not relevant

9.2 Important information on health and safety and environmental protection:

Safety related basic data, methods, and comments

10. Stability and reactivity

Stable under normal conditions of use, storage, and transport

10.1 Conditions to be avoided:

None

10.2 Materials to be avoided:

None

10.3 Dangerous decomposition products:

None

11. Toxicological information

11.1 Toxicokinetics, metabolism and distribution:

Oral uptake < 0.1%, nearly insoluble in lung fluids, most absorbed aluminium oxide is rapidly excreted through urine, main deposit in body is in bone structure.

11.2 Acute effects (acute toxicity, irritation and corrosivity):

No acute effects

11.2.1 Acute toxicity:

LD50 (oral): 				> 5000mg/kg bwt (rats)

LD50 (dermal): 				No effect

LC50 (inhalation): 			> 5 mg/l(rats)

11.2.2 Specific symptoms in animal tests:

After swallowing:	 			None

After skin contact: 			None

After inhalation: 				None

11.2.3 Irritation and Corrosive effects:

Irritant effects on skin:			No effects

Irritant effect on eyes: 	No effects apart from mechanical irritation.

11.3 Sensitisation:

After skin contact: 			None

After inhalation: 				None

Remarks:

11.4 Toxicity after repeated intake (sub acute, sub chronic, chronic):

Sub acute oral Toxicity: 			None, Calculated DNEL 6,2 mg/kg bwt/day

Sub acute inhalation Toxicity: 		None, see occupational exposure limits, calculated DNEL:15,6 mg/m3  respirable

Assessment:

11.5 CMR-effects (carcinogenic, mutagenic and reproductive effects)

Carcinogenicity: 				None

Mutagenicity: 				None

Reproductive toxicity: 			None

Assessment of CMR properties:	 	Not classified for CMR

Product components not listed under IARC/NTP/ACGIH (ingredient carcinogenicity)

11.6 Practical experience:

Observations relevant for classification: 	none

Other observations: 	none

12. Ecological Information

12.1 Ecotoxicity:

| Product/ingredient name | test | result | Species | Exposure |
| --- | --- | --- | --- | --- |
| Aluminium oxide | Fish - OECD TG 203 | >100 mg/l | Salmo trutta | pH 8 |
| Aluminium oxide | Daphnia - OECD TG 202 | >100mg/l | Daphnia Magna | pH 8 |
| Aluminium oxide | Algae - OECD TG 201 | >100mg/l | Selenastrum Capricornutum | pH 8 |

12.2 Mobility: 				Not mobile under normal environmental conditions may be leached from the ground at low pH (< 5.5) or high pH (> 8.5).

12.3 Persistence and degradability:

12.3.1 Persistence:			Not relevant for metals

12.3.2 Biological degradability:		Not degradable

12.4 Bioaccumulative potential:		Not bio accumulative

12.5 Long term ecotoxicity: 		Not classified for ecotoxicity

12.6 Results of PBT assessment:		Not relevant for metals

12.7 Other adverse effects:		No

12.8 Final assessment:	 No acute or chronic classification is appropriate for Al metal massive based on non toxic results below the Ecotoxicity Reference Value (ERV) of tests with aluminium metal, oxide and hydroxide at loadings of 100 mg/L  at pH 8-8.5 (maximum solubility of Al expected).

All aluminium in soil or the aquatic environment comes from natural sources. Local sources has an insignificant contribution and impact on environment

13. Disposal considerations

13.1 Disposal / Waste (Product):

Dispose of wastes and residues in accordance with local waste regulations

13.2 Packaging:

Not relevant

14. Transport information

Not regulated

15. Regulatory Information

No classification or special regulations. Follow general rules for handling, transport and waste management.

Chemical Safety Assessment carried out.

16. Other information

In dealing with chemicals the national laws and regulation must be observed and applied.

This information is based on our present knowledge. However, this shall not constitute a guarantee for any specific product features and shall not establish a legally valid contractual relationship

Recommended limitations of use by manufacturer:

For industrial use and as component in consumer products.

Version history:

Original: 2010-08-23 (new)

Revision: -

Doc.-ID:

Department issuing MSDS:

Health/Safety: xxx

Abbreviations and acronyms:

ACGIH 	American Conference of Governmental Industrial Hygienists

OSHA 	Occupational Safety and Health Administration (US)

ADR: 	Accord européen sur le transport des marchandises dangereuses par Route (European Agreement concerning the International Carriage of Dangerous Goods by Road)

RID: 	Règlement international concernant le transport des marchandises dangereuses par chemin de fer (Regulations concerning the International Transport of Dangerous Goods by Rail)

IMDG: 		International Maritime Code for Dangerous Goods

IATA: 		International Air Transport Association

IATA-DGR: 	Dangerous Goods Regulations by the "International Air Transport Association" (IATA)

ICAO: 		International Civil Aviation Organization

ICAO-TI: 		Technical Instructions by the "International Civil Aviation Organization" (ICAO)

GHS: 		Globally Harmonized System of Classification and Labelling of Chemicals

EINECS: 		European Inventory of Existing Commercial Chemical Substances

CAS: 		Chemical Abstracts Service (division of the American Chemical Society)

Bwt		bodyweight

PNEC		Potential No Effect Concentration

DNEL		Derived No Effect Level

DOC		Dissolved Organic Compounds